## Slide 1
ISEN 614 Advanced Quality Control
Fall 2016 Project
Dwarkanath Prabhu
Venkata Kartik Mutya
Industrial & Systems Engineering
Texas A&M University
1/10
ISEN 614
Texas A&M

## Slide 2
Understanding the Problem
2/10
ISEN 614
Texas A&M
The problem at hand has 552 samples, each with 209 data points.
n = 552
p = 209
This can be denoted as {}, j = 1,…, 552 and each is a 209 x 1 vector. The task at hand is to identify in-control and out-of-control samples.
The and for this data are not known. Hence, this is a Phase I analysis with a sample size of 1. We will use and S to estimate and
Since the number of dimensions is very high, we will first reduce data using principal component analysis and then use the Hotelling chart to isolate in-control data.

## Slide 3
Data Reduction (1/3)
For principal component analysis, we need and S for the sample.
Sample statistics:
We will calculate eigenvalues and eigenvectors of S to find the reduced dimension. These eigenvectors will be used to form principal components from the original data
3/10
ISEN 614
Texas A&M

## Slide 4
Data Reduction (2/3)
4/10
ISEN 614
Texas A&M
For the S matrix, we calculate the eigenvalues and arrange them in descending order.
We plot a graph using the formula:
MDL (l) = n(p-l)log( + l(2p – l)log(n)/2
Where are the arithmetic and geometric means respectively of the smallest (p – l) eigenvalues.
From the graph of MDL values plotted against l, the value of l for which MDL is minimum is 35.

## Slide 5
Data Reduction (3/3)
5/10
ISEN 614
Texas A&M
35 is still a very large number. Hence we look at the scree plot i.e. the plot of eigenvalues against the number of principal components
From the scree plot, it can be seen that there is a bend where the x-axis value is 4. We will thus choose only the first 4 principal components for our analysis.

## Slide 6
Principal Component Analysis
6/10
ISEN 614
Texas A&M
For Principal Component Analysis (PCA), we calculate the vector y, such that
Where i = 1,..,4 and is the eigenvector of S.
As there are n (= 552) samples, there are n such y vectors of length 4 each.
We will now perform Phase I analysis on y.

## Slide 7
Phase I Analysis
For Phase I analysis of y, we approximate the upper control limit using
Here, we have chosen α = 0.05. p is the reduced dimension, hence p = 4. This value comes to 9.49
We will now plot the Hotelling statistic for each sample. To isolate in-control data, we will remove out-of-control samples and recalculate the statistic till we are left with only in-control samples.
To calculate statistic, we use:
Where is the mean of y, S is the covariance matrix of y and j is the sample number. These can be calculated the same way as we did for x on Slide 3.
7/10
ISEN 614
Texas A&M

## Slide 8
Hotelling Statistic First Iteration
8/10
ISEN 614
Texas A&M
In this plot, it can be seen that there are several samples that are out of control

## Slide 9
Hotelling Statistic In-Control Samples
9/10
ISEN 614
Texas A&M
In this plot, all samples are in control. In total there are 461 in-control samples.

## Slide 10
Thank You
10/10
ISEN 614
Texas A&M